## Slide 1: Vector processors:
Department of Electrical Engineering Stanford University
Christos Kozyrakis
Vector Processors

## Slide 2: Announcements
Readings for this lecture
  H&P 4th edition, Appendix F
  Required paper
HW3 available on online
  Due on Wed 11/11th
Exam on Fri 11/13, 9am - noon, room 200-305
  All lectures + required papers
  Closed books, 1 page of notes, calculator
  Review session on Friday 11/6, 2-3pm, Gates Hall Room 498

## Slide 3: Review: Multi-core Processors
Use Moore’s law to place more cores per chip
  2x cores/chip with each CMOS generation
  Roughly same clock frequency
  Known as multi-core chips or chip-multiprocessors (CMP)
Shared-memory multi-core
  All cores access a unified physical address space
  Implicit communication through loads and stores
  Caches and OOO cores lead to coherence and consistency issues

## Slide 4: Review: Memory Consistency Problem
Intuitively, you expect to print A=1
  But can you think of a case where you will print A=0?
  Even if cache coherence is available
Coherence talks about accesses to a single location
Consistency is about ordering for accesses to difference locations
Alternatively
  Coherence determines what value is returned by a read
  Consistency determines when a write value becomes visible
P1
P2
/*Assume initial value of A and flag is 0*/
A = 1;
flag = 1;
while (flag == 0); /*spin idly*/
print A;

## Slide 5: Sequential Consistency (What the Programmers Often Assume)
Definition by L. Lamport:
– A system is sequentially consistent if the result of any execution is the same as if (a) the operations of all processors were executed in some sequential order, and (b) the operation of each individual processors appear in the order specified by the program.
What does SC mean for an OOO processor with caches?
–
Any extra requirements on top of data flow dependencies?

## Slide 6: Alternative 1: Relaxed Consistency Models
Vector processors - 6
Relax some of the SC ordering requirements
  In hope of higher performance from hardware
  But must be careful about programming implications
Example: processor consistency (Intel) or total store order (Sun)
  A read can commit before an earlier write from the same core (with different address) or from another core (to any address) is visible
  Allows for FIFO store buffers
    Loads can bypass a buffered store to a different address
Example: relaxed consistency (IBM)
  Relax all read/write orderings
  SW inserts memory barriers (fences) to enforce order when truly needed
    Can be tricky

## Slide 7: Alternative 2: Use HW Speculation Mechanisms
Reorder loads and store aggressively but track for SC violations
  Check point: when load or store is committed from the ROB
Executing loads early
  Must ensure that when load commits the value read is still valid
  Keep a table with speculatively read values and flag a violation if a write to same value is written by other threads
Reordering stores early
  Acquire exclusive access to cache line asap
  Check if in exclusive state again when at the head of the ROB

## Slide 8: Put It All Together: The CPU-Memory Interface

## Slide 9: Synchronization and Mutual Exclusion
Motivation
  How to ensure that :22 concurrent processes cannot simultaneously access the same data or execute same code
  Needed for parallel programs or programs that share data and OS services
    E.g. two editor processes updating the same file
Can we use regular load/store instructions to do mutual exclusion?
L1: load flag;
If (flag == 0) store flag=1; else goto L1;
Work(); /* need exclusive access */ store flag=0;
  Does this work correctly on single-core or multi-core?
    Assume cache coherence and sequential consistency

## Slide 10: HW Support for Mutual Exclusion & Synchronization
Atomic instructions: many flavors, same goal – Atomic exchange
  Atomically exchange values in register – memory location
Atomic test & set instruction
  Test if value is 0 and set to 1 if test is successful
Atomic compare & swap instruction
  Test if value is 0 and set it to other value if test is successful
Atomic fetch and increment
  Read old value and store +1
Load-linked and store-conditional instructions
  LL: Load & remember old value
  SC: Store if old value still in memory
Implementation: need support from CPU, caches, and memory controller
Can be used to implement higher level synchronization constructs
– Locks, barriers, semaphores, … (see CS140 & CS315A)

## Slide 11: Our Simple Example Revisited
New version assuming atomic exchange
– Initial value of Reg=1 and flag=0
L1: atom_exchange Reg, flag; If (Reg == 1) goto L1;
Work(); /* exclusive access */ Reg = 1;
store flag = 0;
Does this work correctly on uniprocessors or multi-processors?

## Slide 12: Example: Implementation of Spin Locks
Spin lock: try to find lock variable 0 before proceeding further
With atomic exchange
try: | li R2,#1 | 
lockit: | lw R3,0(R1) | #load var
 | bnez R3,lockit | #not free=>spin
 | exch R2,0(R1) | #atomic exchange
 | bnez R2,try | #already locked?
With Load-linked & Store-conditional
lockit: | ll R2,0(R1) | #load linked
 | bnez R2,lockit | #not free=>spin
 | li R2,#1 | #locked value
 | sc R2,0(R1) | #store
 | beqz R2,lockit | #branch if store fails

## Slide 13: Vector Processors

## Slide 14: Vector Processors
Scalar processors operate on single numbers (scalars)
Vector processors operate on vectors of numbers
– Linear sequences of numbers
r1
r2
r3
SCALAR
(1 operation)
+
add r3, r1, r2
v1 v2
+
v3
vector length
vadd.vv v3, v1, v2
VECTOR
(N operations)

## Slide 15: What’s in a Vector Processor
A scalar processor (e.g. a MIPS processor)
  Scalar register file (32 registers)
  Scalar functional units (arithmetic, load/store, etc)
A vector register file (a 2D register array)
  Each register is an array of elements
  E.g. 32 registers with 32 64-bit elements per register
  MVL = maximum vector length = max # of elements per register
A set for vector functional units
  Integer, FP, load/store, etc
    Some times vector and scalar units are combined (share ALUs)

## Slide 16: Example Vector Processor

## Slide 17: Basic Vector Instructions
Instr. | Operands | Operation | Comment
VADD.VV | V1,V2,V3 | V1=V2+V3 | vector + vector
VADD.SV | V1,R0,V2 | V1=R0+V2 | scalar + vector
VMUL.VV | V1,V2,V3 | V1=V2*V3 | vector x vector
VMUL.SV | V1,R0,V2 | V1=R0*V2 | scalar x vector
VLD | V1,R1 | V1=M[R1...R1+63] | load, stride=1
VLDS | V1,R1,R2 | V1=M[R1…R1+63*R2] | load, stride=R2
VLDX | V1,R1,V2 | V1=M[R1+V2i,i=0..63] | indexed("gather")
VST | V1,R1 | M[R1...R1+63]=V1 | store, stride=1
VSTS | V1,R1,R2 | V1=M[R1...R1+63*R2] | store, stride=R2
VSTX | V1,R1,V2 | V1=M[R1+V2i,i=0..63] | indexed(“scatter")
+ all the regular scalar instructions (RISC style)…

## Slide 18: Vector Code Example
32 element SAXPY: scalar |  | 32 element SAXPY: vector |  | 
LD | F0, a | LD | F0,a | #load a
ADDI | R4, Rx,#256 | VLD | V1,Rx | #load X[0:31]
L: LD | F2, 0(Rx) | VMULD.SV | V2,F0,V1 | #vector mult
MUL.D LD ADD.D | F2, F0, F2 F4, 0(Ry) F4, F2, F4 | VLD VADDD.VV VST | V3,Ry V4,V2,V3 Ry,V4 | #load Y[0:31] #vector add #store Y[0:31]
SD | F4, 0(Ry) |  |  | 
ADDI | Rx, Rx, 8 |  |  | 
ADDI | Ry, Ry, 8 |  |  | 
SUB | R20,R4,Rx |  |  | 
BNZ R20,L
Y[0:31] = Y[0:31] + a*X[0:31]

## Slide 19: Vector Length
A vector register can hold a maximum number of elements
  Maximum vector length or MVL
What to do when the application vector length is not exactly MVL?
Vector-length (VL) register controls the length of any vector operation, including a vector load or store
  E.g. vadd.vv with VL=10 is
  for (i=0; i<10; i++) V1[i]=V2[i]+V3[i]
VL can be anything from 0 to MVL
  Set it before each instruction or group of instructions
How do you code an application where the vector length is not known until run-time?

## Slide 20: Strip Mining
Suppose application vector length > MVL
Strip mining
  Generation of a loop that handles MVL elements per iteration
  A set operations on MVL elements is translated to a single vector instruction
Example: vector SAXPY of N elements
  First loop handles (N mod MVL) elements, the rest handle MVL
VL = (N mod MVL);
for (i=0; i<VL; i++) Y[i]=a*X[i]+Y[i];
low = (N mod MVL); VL = MVL;
for (i=low; i<N; i++)
//set VL = N mod MVL
//1st loop is a single set of
// vector instructions
// set VL to MVL
// 2nd loop requires N/MVL
Y[i]=a*X[i]+Y[i]; // sets of vector instructions

## Slide 21: Advantages of Vector ISAs
Compact: single instruction defines N operations – Also reduces the frequency of branches
Parallel: N operations are (data) parallel
  No dependencies
  No need for complex hardware to detect parallelism (similar to VLIW)
  Can execute in parallel assuming N parallel datapaths
Expressive: memory operations describe patterns
  Continuous or regular memory access pattern
  Can prefetch or accelerate using wide/multi-banked memory
  Can amortize high latency for 1st element over large sequential pattern

## Slide 22: Vector Optimization 1: Chaining
Suppose the following code with VL=32:
V1,V2,V3 V4,V1,V5
vmul.vv vadd.vv
Chaining
# very long RAW hazard
vadd
vmul
vadd
V1 is not a single entity but a group of individual elements
Pipeline forwarding can work on an element basis
Flexible chaining: allow vector to chain to any other active vector operation => more read/write ports
Unchained
vmul
Chained

## Slide 23: Vector Optimization 2: Multiple Datapaths per Functional Unit
vadd.vv V3,V2,V1 (VL=N)
V2[3]
V2[2]
V2[1]
V1[3]
V1[2]
V1[1]
+
V3[1]
V2[9] V1[9]
V2[5] V1[5]
V2[13] V1[13] V2[13] V1[13] V2[14] V1[14] V2[15] V1[15]
+
V3[0]
V2[9] V1[9] V2[10] V1[10] V2[11] V1[11]
V2[5] V1[5] V2[6] V1[6] V2[7] V1[7]
+
V3[1] V3[2]
4 elements/cycle N/4 cycles
4 adders
+
+
V3[3]
1 element/cycle N cycles
1 adder

## Slide 24: Vector Optimization 2+: Multiple Lanes
To/From Memory System
Elements for each vector register interleaved across the lanes
Each lane receives identical control
Multiple element operations executed per cycle
Modular, scalable design
No need for inter-lane communication for most vector instructions
Pipelined Datapath
Functional Unit
Lane
Vector Reg.
Partition
Elements
Elements
Elements
Elements

## Slide 25: Chaining & Multi-lane Example
VL=16, 4 lanes,
2 FUs, 1 LSU
chaining -> 12 ops/cycle
Just 1 new instruction issued per cycle
!!!!
vld vmul.vv vadd.vv addu vld vmul.vv vadd.vv addu
LSU
FU0
FU1
Scalar
Time
Element Operations:
Instr. Issue:

## Slide 26: Vector Optimization 3: Conditional Execution
Suppose you want to vectorize this:
for (i=0; i<N; i++) if (A[i]!= B[i]) A[i] -= B[i];
Solution: vector conditional execution
  Add vector flag registers with single-bit elements (masks)
  Use a vector compare to set the a flag register
  Use flag register as mask control for the vector sub
    Add executed only for vector elements with corresponding flag element set
Vector code |  |  | 
vld | V1, | Ra | 
vld | V2, | Rb | 
vcmp.neq.vv | M0, | V1, V2 | # vector compare
vsub.vv | V3, | V2, V1, M0 | # conditional vadd
vst | V3, | Ra | 
Conditional execution & multiple lanes
– Can you skip masked element operations without intra-lane communication?

## Slide 27: Making a Vector Processor Multimedia-ready (From Supercomputing to Embedded in 3 Easy Steps)
Support narrow data types
  Allow each vector registers to store 64, 32, or 16-bit elements
  Use a control register to indicate the width of elements in registers
Support saturated and fixed-point arithmetic
  Minor twist to functional units
Support element permutations for vectorized reductions
  for (i=0; i<N; i++) S += A[i]
  Rewrite as
    for (i=0; i<N; i+=VL) S[0:VL-1] += A[i:i+VL-1];
    for (i=0; i<VL; i++) S+=S[i];
  First loop is trivially vectorizable
  Can vectorize 2nd loop with a permutation instruction that splits the elements of a vector register into two registers
    Continue the binary-tree approach to reductions

## Slide 28: VIRAM Architecture State
General Purpose Vector Registers
Vector Flag Registers
vr0 vr1
vr31
vf0 vf1
vf15
1 bit
Element width is 64b, 32b, or 16b
More elements per vector register for narrow data
r0 r1
r15
64 bits
Scalar Registers

## Slide 29: Example: DSP Support in the VIRAM ISA
EE382A – Autumn 2009
Christos Kozyrakis
Vector processors - 29
29
Support for fixed-point numbers, saturation, rounding modes
Multiply-add model for efficient compilation
Simple instructions for intra-register permutations for reductions and butterfly operations
– High performance for dot-products and FFT without the complexity of a random permutation
sat
Round
a
w
y
z
+
*
x
n/2
n/2
n
n
n
n

## Slide 30: Putting it All: Vector IRAM Prototype Vectors + Embedded DRAM
VIRAM media processor
  125M transistors
  200MHz, 2 Watt
Embedded DRAM
13 Mbytes
8 banks
6.4GB/sec per bank (peak)
Processor
  4-lane vector processor
    6.4 Gop/sec
  64-bit MIPS core
DRAM | DRAM | DRAM | DRAM
 |  | DRAM | DRAM | DRAM | DRAM
MIPS CPU |  |  |  |  | 
I/O |  | crossbar
crossbar
Vector Control |  | Lane 0 |  | Lane 1 |  | Lane 2 |  | Lane 3

## Slide 31: Other Interesting Vector Instructions: Compress, Expand, PopCount, …
Compress
  Pack all the non-masked elements of an input vector register into the first few elements of a destination vector register
Expand (reverse of compress)
  Distribute the first few elements of the input register into the non-masked elements of the destination vector register
  Compress & expand used for dense execution of conditional operations
PopCount
  Count the number of non-masked elements in a vector
FindFirstOne, FineLastOne, …
  Find # of first non-masked element, etc
SetBeforeFirstOne, SetIncludingFirstOne, …
  Create a mask register with 1s up to the first 1 in the source register, etc
Insert, extract
  Move single vector element to/from scalar register

## Slide 32: Automatic Vectorization
// Matrix-matrix multiply: c[i][j]=SUM(a[i][t]*b[t][j]) for (i=1; i<n; i++) {
for (j=1; j<n; j++) { sum = 0;
for (t=1; t<n; t++) {
sum += a[i][t] * b[t][j]; // dependence
}
c[i][j] = sum;
}
}
Which loop to vectorize?
  Inner loop and outer loop vectorization
  See any tradeoffs?
Automatic vectorization requires extensive capabilities for dependence analysis

## Slide 33: Which Applications Fit the Vector Model?
Vectors are great when we have data-level parallelism (DLP)
  Most efficient way to exploit DLP
  Remember, we can exploit DLP as ILP or TLP
    On a superscalar or multiprocessor
Which applications have DLP?
  Scientific computing
    Weather forecast, car-crash simulation, biological modeling
    Vector processors were invented for this purpose (supercomputers)
  Multimedia computing
    Speech, image, and video processing
    Identical operations execution on streams or arrays of sound samples, pixels, and video frames
    The reason for the recent revival of vector architectures
    Multimedia on embedded devices
– Need high performance @ low power @ low complexity @ small code size

## Slide 34: The Timeline of Vector Processors
Widely used for supercomputing systems in the 70s – 90s
  Cray, CDC, Convex, TI, IBM, ..
Fell out of fashion in the 80s and 90s
  Difficult to fit a vector processor in a single chip
  Building supercomputers out of commodity microprocessors
Remaining vector supercomputer: NEC SX-9
  8 lanes (5 functional unites), 8+64 vregs (256 elements/reg), 3.2GHz
But now vectors are making a come back
  Short vectors in all ISAs (SIMD), Intel Larabee, …
  Why?

## Slide 35: Vector Power Consumption
Can trade-off parallelism for power
  Power = C *Vdd2 *F
  If we double the lanes, peak performance doubles
  Halving F restores peak performance but also allows halving the Vdd
  Powernew = (2C)*(Vdd/2)2*(f/2) = Power/4
Simpler logic for large number of operations/cycle
  Replicated control for all lanes
  No multiple issue or dynamic execution logic
Simpler to gate clocks
  Each vector instruction explicitly describes all the resources it needs for a number of cycles
  Conditional execution leads to further savings

## Slide 36: SIMD Extensions for Superscalar Processors
Every CISC/RISC processor today has SIMD extensions
  MMX, SSE, SSE-2, SSE-3 3D-Now, Altivec, VIS, …
Basic idea: accelerate multimedia processing
  Define vectors of 16 and 32 bit elements in regular registers
  Apply SIMD arithmetic on these vectors
Nice and cheap
  Don’t need to define big vector register file
    Takes up area and complicates exceptions
  All we need to do
    Add the proper opcodes for SIMD arithmetic
    Modify datapaths to execute SIMD arithmetic
  Certain operations are easier on short vectors
    Reductions, random permutations

## Slide 37: Example of Simple SIMD Instruction
+
+
+
+
SIMD ADD
64-bit reg. 64-bit reg.
64-bit reg.

## Slide 38: Example of Fancy SIMD Instruction
*
*
*
*
+
+
Sum of Partial Products
64-bit reg. 64-bit reg.
64-bit reg.
temp. result

## Slide 39: Loading & Storing SIMD Values
Typical case: no vector-like loads & stores
  Must use regular 64-bit load/store instructions
  Problems: data-sizes, alignment, strides
Solution: multiple load/stores & manipulation instructions
  Pack & unpack
    To solve problems with data sizes
  Rotate & shift
    To solve problem with alignment

## Slide 40: Problems with SIMD Extension
SIMD defines short, fixed-sized, vectors
  Cannot capture data parallelism wider than 64 bits
  Must use wide-issue to utilize more than 64-bit datapaths
  SSE and Altivec have switched to 128-bits because of this
SIMD does not support vector memory accesses
  Strided and indexed accesses for narrow elements
  Needs multi-instruction sequence to emulate
    Pack, unpack, shift, rotate, merge, etc
  Cancels most of performance and code density benefits of vectors
Compiler support for SIMD?
  They change too often…

## Slide 41: Superscalar+SIMD Vs. True Vectors: Example
QCIF and CIF numbers are in clock cycles per frame
All other numbers are in clock cycles per pixel
MMX results assume no first level cache misses
 | Vector | MMX
iDCT | 0.75 | 3.75 (5.0x)
Color Conversion | 0.78 | 8.00 (10.2x)
Image Convolution | 1.23 | 5.49 (4.5x)
QCIF (176x144) | 7.1M | 33M (4.6x)
CIF (352x288) | 28M | 140M (5.0x)

## Slide 42: Intel Larrabee:
2-way issue, in-order cores with vector capabilities
• + 4-way multithreaded
Cores communicate on a wide ring bus
L2 cache is partitioned among the cores
  Provides high aggregate bandwidth
  Allows data replication & sharing
Memory Controller
Multi- Multi-
Threaded Threaded
Wide SIMD Wide SIMD
Multi- Multi-
Threaded Threaded
Wide SIMD Wide SIMD
Memory Controller
Texture Logic Fixed Function
System Interface Display Interface
Memory Controller
Multi-Threaded Multi-Threaded
Wide SIMD Wide SIMD
I$ D$ I$ D$
Multi-Threaded Wide SIMD
I$ D$
Multi-Threaded Wide SIMD
I$ D$
Microarchitecture (Larrabee)
L2 Cache
A Single-Chip Vector Multiprocessor
. . .
. . .

## Slide 43: Larrabee x86 Core Block Diagram
Separate scalar and vector units with separate registers
In-order x86 scalar core
Vector unit: 16 32-bit ops/clock
Short execution pipelines
Fast access from L1 cache
Direct connection to each core’s subset of the L2 cache
Prefetch instructions load L1 and L2 caches
Instruction Decode
Scalar Unit
Vector Unit
Scalar Registers
Vector Registers
L1 Icache & Dcache
256K L2 Cache Local Subset
Ring
Microarchitecture (Larrabee)

## Slide 44: Larabee Vector Unit Block Diagram
Vector complete instruction set
  32 vector registers (512 bits), 8 mask registers
  Scatter/gather for vector load/store
  Mask registers select lanes to write, which allows data-parallel flow control
  This enables mapping a separate execution kernel to each VPU lane
Vector instructions support
  Fast read from L1 cache
  Numeric type conversion and data replication while reading from memory
  Rearrange the lanes on register read
  Fused multiply add (three arguments)
  Int32, Float32 and Float64 data
Mask Registers
16-wide Vector ALU
Replicate
Reorder
Vector Registers
Numeric Convert
Numeric Convert
L1 Data Cache

## Slide 45: Summary
Vector processors
  Processors that operate on linear sequences of numbers
    Vector add, vector load, vector store, …
  Can express and exploit data-level parallelism in applications
SIMD extension
  Short vector extensions for ILP processors
  Get some of the advantages of vector processors without most of the cost
Remember what Jim Smith said:
  “The most efficient way to execute a vectorizable applications is a vector processor”